### Information request for quotation

Name:  Robert van Schoubroeck

Date of request: 18-12-2012

Please quote before: 11-01-2012

Short description of function: Assy Wheel is base of runner for lineaire guide system.

Typical temperature: -20 to +100C.

Quotation information:

| Article number | N.A. |
| --- | --- |
| Article name | Wheel assy |
| Attached files | E000008142.pdf |
| Accuracy of quote | exact calculation / estimation |
| Order duration | 5 years |
| Quantity / year | 60 000 |
| Batch size | Quote batch of 10 000 |
| Lead time | Please specify lead time. |
| Shipment | DDP |
| Charge of tooling cost | Single payment |
| Packaging | Please advise, max weight 18kg. |
| Number of FOT/samples | 200 pieces |
| Product improvement proposals | Are welcome |
| Tracibility of product | Standard ISO 9000 requirements. |
| Special remarks | Fully hardened balls No/little play in bearing Stainless steel components (ANSI 304 or comparable) Foodgrade lubricated. Water resistant seals (2 RS) Dyn load rating C > 1500 N Static load rating Co > 750 N Axial load performance as good as possible |
| MPDS and MSDS | Please attach MPDS and MSDS of lubricant to quotation. |

Quality information:

| Required customer rejection level | < 50 ppm |
| --- | --- |
| Measurement report of FOT | Yes |
| CE approved | No |
| Required certificates | None |

Tooling requirements:

| Draft angle | N.A. |
| --- | --- |
| Gate position | N.A. |
| Mould separation | N.A. |
| Position of ejectors | N.A. |
| Number of cavities | N.A. |